DDIT
Department of Civil Engineering

Irrigation Engineering Handout

(Course Code: 5709)

Academic Year: 2007 E.C.

Chapter 1: Introduction

1.1 Irrigation – History, Definition and Necessity

- Water is the most precious and vital resource of humanity

- Our survival entirely depends on the availability of water at the surrounding

- Where dose water originally come from?

- Recent studies indicated it evolved from the inner surface of Mother Earth

- We are made of cells constituting 80% of water

- Therefore our existence is real through the availability of this incredible molecule of water connecting us to the surrounding we live

- We live in the world of growing population, every nation strives to feed its people

- Hence the largest proportion of available water is used for irrigation so as to satisfy the existing demand for food production

- Since mankind domesticated crops to feed himself he normally gets water under natural process, either through direct rain or subsided floods

- But his harvest is dependent upon the mercy of nature

- there  may be heavy rainfall resulting floods attributed to serious damage on crops, or

- there  may not be rains at all creating scarcity and drought

- Thousands years ago, to tackle this challenge man discovered various methods to store and harness water for irrigation purpose

- Historically ancient civilization flourished alongside the development of irrigation system

- Irrigation began at around 6000BC in Egypt and Mesopotamia (present day Iraq and Iran) using the water of the flooding Nile or Tigris/Euphrates rivers.

- The flood waters were diverted to fields for 40 to 60 days. It was then drained back into the river at the right moment in the growing cycle.

- The first major irrigation project was created during Egypt’s First Dynasty.  They built dams and canals to use the diverted flood waters of the Nile into a new lake.

- The Pharaohs became powerful boosting their harvest using Nile for irrigation,

- The monument Giza’s Pyramids are footprints of the Nile

Definition of Irrigation

- As human beings do plants require water and air for their survival,  different types of plants require different quantities of water during different times

- Irrigation can be defined as the science of artificial application of water to the land in accordance with the crop requirements throughout the crop growth period for the full-fledged nourishment of the crops.

- Irrigation Engineering refers to the science and technology of planning and designing a water supply system for agricultural land to protect the crops from bad effect of unreliable or low rainfall.

- Irrigation Engineering embraces the bio-system, hydrology and physical structures. It includes the design and construction of weir, dams, canal system for regular supply of water.

Necessity or need of Irrigation

- The following factors governs the necessity of irrigation

- Insufficient rainfall:- when the seasonal rainfall is less than the minimum requirement of crops for satisfactory growth

- Uneven distribution of distribution:- when the seasonal rainfall is not evenly distributed during the crop period or across the cultivable area

- Improvement of perennial crops:- crops like sugarcane, cotton and tree fruits which their crop period is more than one year require water throughout major part of a year beyond the rainy season

- Development of agriculture in desert areas:- In desert areas where rain is very limited irrigation is required for agricultural production

1.2 Advantages and Disadvantages of Irrigation

Advantages /Benefits/ of Irrigation

- Sustaining food security – avoiding the recurrent of drought and famine

- Enable cultivation of cash crops – having economic advantage

- Improve production and productivity of a land – irrigation assures growing two or more crops twice a year

- Feasible for land consolidation, cooperatives and mechanized farming

- Suitable for multi-purpose integration of development projects- (such as hydro-electric generation, flood control, water supply, fishery, access road and communication)

Disadvantages /side-effects/ of Irrigation

- Alkalinity problem and suffocation of crops – excessive seepage and leakage  from the bed and banks of the irrigation canals could result in raised water table and the formation of salinity

- Health hazard – it could be source of malaria and cold

- High initial investment

- However, now a time climate change is eminent the development of  irrigation is not questionable at any cost.

1.3 Types of Irrigation

- Irrigation can broadly classified as

1. Surface irrigation – water is applied over the ground to wet the top surface of soil

> water is usually supplied to main land from higher sources through gravitational force (gravity irrigation)

> water is lifted up by mechanical or manual means from  lower sources (pump irrigation)

2.  Sub-surface irrigation – water is applied below the soil surface to nourish the root zone through capillary action

> laying an artificial openings

> collecting water in the ditch to percolate

Under common practices, irrigation systems can be classified as Lift  irrigation and Flow irrigation.

Lift Irrigation

Flow irrigation

Under inundation irrigation system the soil is kept submerged by thoroughly flooding so as to cause thorough saturation of land and hence it also named as flood irrigation.

The difference between weir, barrage and dam

1.3 Methods of Distribution of Irrigation Water

1.4 Irrigation Development Status in Ethiopia

- Ethiopia covers an area of 1.13 million km2, of which 99.3 percent is a land area and the remaining 0.7 percent is covered with water bodies of lakes.

- It has an arable land area of 10.01 percent and permanent crops covered 0.65 percent.

- Though agriculture is the dominant sector, most of Ethiopia’s cultivated land is under rain-fed agriculture cultivating small fragmented land.

- Due to lack of water storage and large spatial and temporal variations in rainfall, there is not enough water for most farmers to produce more than one crop per year

- Hence there are frequent crop failures due to dry spells and droughts especially in arid and semi-arid areas.

- The country has 12 river basins. The total mean annual flow from all the 12 river basins is estimated to be 122 BMC (Billion Metric Cube)

- As compared to surface water resources, Ethiopia has lower ground water potential estimated to be about 2.6-13.2 BMC, 50% could be extractable

- Estimates of the irrigated area presently vary, but range between 150,000 and 250,000 hectares, less than five percent of potentially irrigable land

- The irrigation area coverage distribution of 38 percent traditional, 20 percent modern communal, 4 percent modern private and 38 percent public schemes

- Relatively, the most utilized river basin and the only river entirely in the country, is Awash river basin.

Map of River Basins of Ethiopia